## Slide 1
Lecture
on
“Advanced Computer Architecture –TCS 704”
by
Akansha Gupta
DEPARTMENT OF COMPUTER SCIENCE AND ENGINEERING
GRAPHIC ERA DEEMED TO BE UNIVERSITY – 248002

## Slide 2: Trends and Predictions
Trend, n.
1: direction of movement: FLOW
2 a: a prevailing tendency or inclination: DRIFT
2 b: a general movement: SWING
2 c: a current style or preference: VOGUE
2 d: a line of development: APPROACH
Webster’s Dictionary
It is very difficult to make an accurate prediction, especially about the future.
Niels Bohr

## Slide 3: Historical Trends and Perspective
Pre-II: Mechanical calculating machine
II - 50’s: Technology improvement
relays → vacuum tubes
high-level languages
60’s: Miniaturization/packaging
Transistors
integrated circuits

## Slide 4
70’s: Semantic gap
complex instruction sets
language support in hardware
microcoding
80’s: Keep It Simple, Stupid
RISC vs CISC
shift complexity to software
90’s: What to do with all of these transistors?
large on-chip caches
prefetching hardware
speculative execution
special-purpose instructions
multiple processors on-a-chip

## Slide 5: What is Computer Architecture?
It has nothing to do with buildings.
Goals of a computer designer
- control complexity
- maximize performance
- minimize cost?
Use levels of abstraction
silicon and metal
→ transistors
→ gates
→ flip-flops
→ registers
→ functional units
→ processors
→ systems

## Slide 6
Architecture
- defines interface between higher levels and software
- requires close interaction between
* HW designer
* SW designer

## Slide 7: Performance Metrics
System throughput
- work per unit time → rate
- used by system managers
Latency
- time taken from beginning to end of a task
Execution time
- how long to execute your application
- used by system designers and users
Texec = n instrs * # cycles/ # instrs * seconds/cycle = n * CPI * Tclock
Example
Texec = 900 M instrs * instr 1.8 cycles/ instrs * 10 ns / cycle= 16.2 sec

## Slide 8: Improving Performance
Texec = Tclock * n * CPI
Improve clock rate, Tclock
Reduce total number of instructions executed, n
Reduce average number of cycles per instruction, CPI

## Slide 9: 1) Improving the Clock Rate
Use faster technology
- BiCMOS, ECL, etc
- smaller features to reduce propagation delay
Pipelining
    reduce the amount of work per clock cycle

## Slide 10
Performance improvement
- reduces Tclock
- overlaps execution of instructions
→ parallelism
Maximum speedup ≤ pipeline depth

## Slide 11: 2) Reduce Number of Instructions Executed
Texec = Tclock * n * CPI
CISC -- Complex Instruction Set Computer
- powerful instrs to reduce instr count complex addressing modes
complex loop, move instructions
- But may increase cycle time, Tclock
RISC --Reduced Instruction Set Computer
- small, simple instruction set
- simpler implementation
→ faster clock
- But must execute more instructions for same work

## Slide 12: 3) Reduce Average Cycles per Instruction
Texec = Tclock * n * CPI
Decreasing CPI ≡ increasing Instructions Per Cycle (IPC)
Texec = Tclock * n * 1/IPC
CPI < 1 → parallelism
- instruction-level
- processor-level

## Slide 13
THANKS
https://youtu.be/cB1EZMrdXpA