## Slide 1
Lecture
on
“Advanced Computer Architecture –TCS 704”
by
Akansha Gupta
DEPARTMENT OF COMPUTER SCIENCE AND ENGINEERING
GRAPHIC ERA DEEMED TO BE UNIVERSITY – 248002

## Slide 2
PIPELINING PERFORMANCE-2

## Slide 3: Important Notes
Note-01:
The aim of pipelined architecture is to execute one complete instruction in one clock cycle.
In other words, the aim of pipelining is to maintain CPI ≅ 1.
Practically, it is not possible to achieve CPI ≅ 1 due to delays that get introduced due to registers.
Ideally, a pipelined architecture executes one complete instruction per clock cycle (CPI=1).

## Slide 4
Note-02:
The maximum speed up that can be achieved is always equal to the number of stages.
This is achieved when efficiency becomes 100%.
Practically, efficiency is always less than 100%.
Therefore speed up is always less than number of stages in pipelined architecture.

## Slide 5
Note-03:
Under ideal conditions,
One complete instruction is executed per clock cycle i.e. CPI = 1.
Speed up = Number of stages in pipelined architecture

## Slide 6
Note-04:
The 5 stage pipelined processor gives the best performance.
Note-05:
In case only one instruction has to be executed, then-
Non-pipelined execution gives better performance than pipelined execution.
This is because delays are introduced due to registers in pipelined architecture.
Thus, time taken to execute one instruction in non-pipelined architecture is less.

## Slide 7
Note-06:
High efficiency of pipelined processor is achieved when-
All the stages are of equal duration.
There are no conditional branch instructions.
There are no interrupts.
There are no register and memory conflicts.

## Slide 8
PRACTICE PROBLEMS BASED ON PIPELINING IN COMPUTER ARCHITECTURE

## Slide 9: Problem-01:
Consider a pipeline having 4 phases with duration 60, 50, 90 and 80 ns. Given latch delay is 10 ns. Calculate-
Pipeline cycle time
Non-pipeline execution time
Speed up ratio
Pipeline time for 1000 tasks
Sequential time for 1000 tasks
Throughput

## Slide 10: Solution-
Given-
Four stage pipeline is used
Delay of stages = 60, 50, 90 and 80 ns
Latch delay or delay due to each register = 10 ns
Part-01: Pipeline Cycle Time-
Cycle time
= Maximum delay due to any stage + Delay due to its register
= Max { 60, 50, 90, 80 } + 10 ns
= 90 ns + 10 ns
= 100 ns

## Slide 11
Part-02: Non-Pipeline Execution Time-
Non-pipeline execution time for one instruction
= 60 ns + 50 ns + 90 ns + 80 ns
= 280 ns
Part-03: Speed Up Ratio-
Speed up
= Non-pipeline execution time / Pipeline execution time
= 280 ns / Cycle time
= 280 ns / 100 ns
= 2.8

## Slide 12
Part-04: Pipeline Time For 1000 Tasks-
Pipeline time for 1000 tasks
= Time taken for 1st task + Time taken for remaining 999 tasks
= 1 x 4 clock cycles + 999 x 1 clock cycle
= 4 x cycle time + 999 x cycle time
= 4 x 100 ns + 999 x 100 ns
= 400 ns + 99900 ns
= 100300 n

## Slide 13
Part-05: Sequential Time For 1000 Tasks-
Non-pipeline time for 1000 tasks
= 1000 x Time taken for one task
= 1000 x 280 ns
= 280000 ns
Part-06: Throughput-
Throughput for pipelined execution
= Number of instructions executed per unit time
= 1000 tasks / 100300 ns

## Slide 14
THANKS
https://youtu.be/iKPxQctzSms