## Slide 1
Lecture
on
“Advanced Computer Architecture –TCS 704”
by
Akansha Gupta
DEPARTMENT OF COMPUTER SCIENCE AND ENGINEERING
GRAPHIC ERA DEEMED TO BE UNIVERSITY – 248002

## Slide 2
Collision free pipeline

## Slide 3: Instruction Dependencies and Hazards
The overlapped execution of instructions can cause potential hazards if operations initiated by instructions i+l, i+2, ... depend on the results from -instruction i whose execution has not yet been completed.
There are four classes of hazards; read after write (RAW), write after read (WAR), write after write (WAW), and read after read (RAR) which may be caused if domains and ranges of any two instructions are not independent.

## Slide 4: Job Sequencing and Collision Prevention
To achieve optimal performance in an arithmetic pipeline, several tasks must be initiated so that they are executed concurrently in the pipeline.
A collision occurs when two or more initiations attempt to use the same stage at the same time.
Job sequencing involves proper task initiations in order to avoid collisions and to achieve maximum throughput.
The number of time units between two job initiations is known as “latency”.
A latency sequence refers to the sequence of latencies between successive initiations. A latency sequence that repeats itself indefinitely forms a latency cycle.
Latency cycles in which each state is used only once are called simple cycles.

## Slide 5
The average latency of a cycle is the sum of its latencies divided by the number of states used.
Latencies that cause collisions between two initiations constitute a forbidden set of latencies which can be determined from the reservation table.
The number of time units between any two entries on the same row of the reservation table is a member of the forbidden set of latencies.
This set is used to create the collision vector which in turn can be used to determine a collision free latency sequence.
It is a binary vector whose size is equal to the largest forbidden latency that may be obtained from the reservation table.
The bits in the collision vector are labeled from right to left.

## Slide 6: A Three Stage Pipeline

## Slide 7: Reservation Table
Displays the time space flow of data through the pipeline for one function evaluation.

## Slide 8: Forbidden and Permissible Latency
Latencies that cause collisions are called forbidden latencies.
In above reservation table 2, 4, 5 and 7 are forbidden latencies
Latencies that do not cause any collision are called permissible latencies.
In above reservation table 1, 3 and 6 are permissible latencies

## Slide 9
Calculating forbidden latency:
  S1= 6-1=5
    =8-1=7
    =8-6=2
    S2 = 4-2=2
S3= 5-3=2
=7-3=4
=7-5=2

## Slide 10
Therefore, Forbidden latency= 5,7,2,4
Arranging in ascending order= 2,4,5,7
(Note: 0 is discarded incase comes in latency.)
Permissible Latency=1,3,6
(Note: We will not take 8 in the permissible latency as we limit to the maximum bit of forbidden latency.)

## Slide 11
Collision Vector: The combined set of permissible and forbidden latencies can be easily displayed by a collision vector, which is an m-bit (m<=n-1 in a n column reservation table) binary vector C=(CmCm-1….C2C1). The value of Ci=1 if latency I causes a collision and Ci=0 if latency i is permissible.
Cx = C7C6C5C4C3C2C1
= 1011010

## Slide 12
thanks
https://youtu.be/qU4IMR9JhlM